## Slide 1: Technology stack of IoT

## Slide 2
The Internet of Things technology stack is a range of standards, technologies, and applications that lead from the mere connection of objects to the Internet to the easiest and the most complex of applications that make use of these connected things and the collected data by them, and the wide variety of steps that are required to power these apps.
There cannot be any likelihood of anything to do with IoT devices and absolutely no reasons to stay connected with the internet without the IoT technology stack. Simply, this stack encompasses all technologies that are required to move from data and devices associated with the Internet of Things to the so-called IoT use cases.

## Slide 3
From far, this looks like something really simple but the different layers of IoT technology stack include different options and technologies for IoT projects. Most importantly, it is not about just putting out a combination of the right technologies across the stack but also about doing this in a secure, cost-efficient, and accurate way.
However, there are all kinds of challenges on the levels of interoperability. Moreover, there are also hurdles when it comes to all of these technology elements being able to communicate with each other, since there are different standards. The challenges become more complicated and bigger to the naked eye when existing and traditionally connected devices are brought in.

## Slide 4: Three layers of this stack.
IoT device level: There cannot be the Internet of Things without accurate actuators, sensors, and IoT devices in general. This is simply because there cannot be IoT in the absence of accurate data.
IoT Gateway: The Internet of Things gateways are known to significantly enhance remote monitoring, data consolidation, enterprise mobility, remote system control, secure data exchange, and remote monitoring. An IoT Gateway connects strongly with the IoT device layer that is a must-have level towards the next steps of actionable business applications and data or consumer applications and services.
IoT Platform layer: This is the layer where we connect with the consumer and business applications and services. The IoT Platform layer is also critical in the overall development of these services and the interconnection and management with the IoT device level and IoT Gateway layers.

## Slide 5: Major components of IOT systems
Physical objects: with embedded software into a hard ware
Hardware: consisting of a microcontroller, firmware, sensor, sensor, control unit, actuators and communication module.
Communication module: software consisting of device API and device interface for communication over the network and communication circuit/ports and middleware for creating communication stacks using 6 LowPAN, CoAP, LWM2M, IPv4, IPv6 and other protocols.
Software for actions on messages, information and commands which the devices receive and then output to the actuators, which enable actions such as glowing LEDs, robotic hand movement etc.

## Slide 6: Sensors
Sensors are known to us long before the concept of the Internet of Things came into existence. We can find different types of sensors in factories, buildings, and much more. In these cases, sensors are parts of the digital data backbone of intelligent and connected solutions. Anything related to IoT and “smart” is built upon sensors and transducers.
Transducers have the ability of converting a signal in the form of energy into a signal in a different form. This, in the context of IoT sensors, means that sensors have the potential of sensing conditions or the environment in or around the IoT device around which they are present and in and around of the physical items to which the sensors are attached.

## Slide 7
Moreover, sensors have the ability of detecting the changes or events in the environments and for the wide range of purposes for which they were initially designed. They then communicate about these changes or events of certain parameters to predefined systems and different kinds of devices that can then make use of this data for analysis, action, and so forth.
Events and factors, among the environmental parameters, which can be sensed by the sensors include parameters like temperature, sound, humidity, light, presence of certain gases or chemical components, occupancy, and much more. Sensors are critical components of the Internet of Things and must be precisely accurate as they are the basic foundations from where the data gets captured to begin with.

## Slide 8: Actuators
From the perspective of the Internet of Things, actuators sit on the control airflow in a smart building, smart home, or smart room or on the radiator. The sensor detects that there is no one in the room and the actuators then get triggered to a reduced temperature for stopping an event or thing.

## Slide 9
Like sensors, actuators are transducers. While sensors emphasize on the capabilities of sensing and sending, actuators are about acting and activating. The actuator receives a signal and then starts to set in motion what is required to be done in order to act within or upon an environment.
In a way, it can be said that the role of an actuator is the opposite of a sensor but as important as the sensors. Actuators, in the scope of Internet of Things, are mostly turning something on or off through the application of force.

## Slide 10: IoT Gateways
IoT gateways in more than just a way can be categorized under IoT devices. An IoT gateway can be software or hardware and usually a combination of both. Considering the IoT gateway functions, it is however ideal to view them as a separate layer.
IoT gateways play an important role on the intersection of devices associated with the Internet of Things in the strict sense. De facto, IoT gateways are used for encryption, connectivity aggregation, and IoT data decryption. It is also used for translating the different protocols that exist in the landscape of the complete IoT technology, edge computing, aggregation of data, remote control and management, and so forth.

## Slide 11: IOT Platform
Most broadly, a platform is software and hardware, which may include an operating environment, storage, computing power, security, development tools, and many other common functions. Platforms are designed to support many smaller application programs that actually solve business problems.
Platforms are helpful because they abstract a lot of common functions away from the specific application logic.

## Slide 12
In the Internet of Things, platforms are designed to deploy applications that monitor, manage, and control connected devices (Exhibit 1). IoT platforms must handle problems like connecting and extracting data from a potentially vast number and variety of endpoints, which are sometimes in inconvenient locations with spotty connectivity.

## Slide 13: Control Units
Most commonly used control unit in IoT consists of a microcontroller unit (MCU) or
A custom chip or core in a VLSI or an SoC
Popular microcontrollers: ATmega 328, ATMega 32u4, ARM Cortex and ARM LPC.

## Slide 14
Internal RAM
Internal Flash and Firmware
Programmable
IO Ports
Processor
Timers
General
Purpose IOs
Serial IO
Ports
ADC
(Analog to digital converter)
Comm. Network Interfaces
PWM
(Pulse width
Modulator)
Micro controller

## Slide 15: Communication Module
Device message-queue
A device message-cache stores the received messages
Protocol handlers:
CoAP, HTTP, MQTT, TLS, DTLS LWM2M, CoAP-SMS, CoAP-MQ,

## Slide 16: Middleware
OpenIoT (open source middleware)
Communication with sensor clouds and Cloud-based ‘sensing as a service
IoTSyS middleware provisioning of communication stack for smart devices using IPv6, oBIX, 6LoWPAN.
CoAP and multiple standards and protocols. The oBIX is standard XML and web services
protocol oBIX (Open Building Information Xchange).

## Slide 17: OS
RIOT: an operating system for IoT devices. supports developer and multiple architectures
Including ARM7, Cortex-M0, Cortex- M3, Cortex-M4, standard x86 PCs and TI MSP430 architectures.

## Slide 18
Raspbian: a popular Raspberry Pi operating system Based on the Debian distribution of Linux.
AllJoyn, open source OS created by Qualcomm Cross-platform OS with APIs available for Android, iOS, OS X, Linux

## Slide 19: Integration, Collaboration and processes and services
Application (Reporting, Analysis, control)
IoT Cloud PaaS and Server for Manage, Acquire, Organise and Analyse
Edge Computing
Data Analysis, Data Abstraction, Data Accumulation and Management
Connectivity (Communication and Processing Units)
IoT Device Software for gather data, enrich and Communication
Connectivity Interface
Edge Computing
IoT device Hardware Physical devices and Controllers
Fig. 1.8 The IOT software architecture

## Slide 20: Arduino Boards
E.g. Arduino Yún
Using Microcontroller ATmega32u4
Includes Wi-Fi, Ethernet, USB port, micro-SD card slot and three reset buttons
Runs Linux

## Slide 21: Intel Galileo
Intel Galileo board
A line of Arduino-certified development boards.
Intel x86, Intel SOC X1000 Quark based System-On-Chip
Power over Ethernet (PoE) and 6 Analog Inputs

## Slide 22: BeagleBoard
Very low power requirement
Card like computer
Can run Android and Linux
Open source Hardware designs and the software for the IoT devices are

## Slide 23: Raspberry Pi
Wi-Fi-connected device
Included code open source RasWIK

## Slide 24: RFID (Radio Frequency ID)
An identification system
Tagging and labelling
Tiny chips: passive, active and battery powered when reader nearby Wireless

## Slide 25: RFID (Radio Frequency ID)
Communication range 10 cm to 200 m
Standard frequency ranges: 120- 150 kHz, 13.56 MHz, 433 MHz and higher in UHF and Microwave regions

## Slide 26: RFID Applications
Tracking and inventory control
Identification in supply chain systems
Access to buildings and road tolls
Secured store center entries
Devices such as RFID based temperature sensors

## Slide 27: WSN network
Defined as a network in which each sensor node connect wirelessly
Capabilities of computations
Data compaction, aggregation and analysis
Each with communication as well as networking capabilities.

## Slide 28: Node Characteristics
Autonomous: Independent computing power and capability to send requests and receive responses, and data forward and routing capabilities.