## Slide 1: M2M to the IoT

## Slide 2
Machine-to-Machine (M2M) communication is a form of data communication that involves one or more entities that do not necessarily require human interaction or intervention in the process of communication.
M2M is also named as Machine Type Communication (MTC) in 3GPP(The 3rd Generation Partnership Project is a standards organization which develops protocols for mobile telephony)

## Slide 3
M2M communication could be carried over mobile networks (e.g. GSM-GPRS, CDMA EVDO networks).
In the M2M communication, the role of mobile network is largely confined to serve as a transport network.

## Slide 4: M2M system
Each machine in embeds a smart device
• Device senses the data or status of the machine
• Performs the computation and communication functions

## Slide 5: M2M system
A device communicates via wired or wireless systems
• Protocols: 6LowPAN, LWM2M, MQTT, XMPP
• Each device assigned 48-bits Ipv6 addresses.

## Slide 6: Architecture and components of M2M
A: M2M Device
Device capable of replying to request for data contained within those devices or capable of transmitting data autonomously.
Sensors and communication devices are the endpoints of M2M applications.
Generally, devices can connect directly to an operator’s network, or they will probably interconnect using WPAN technologies such as ZigBee or Bluetooth.
Backhaul to an operator’s network is than achieved via gateways that encapsulate and manage all devices.
Consequently, addressing and identifying, e.g., routing, of the devices relies heavily on the gateways.
Devices that connect via gateways are normally outside the operator’s responsibility but belong to M2M applications that are provided by service or application providers.
Sensors and devices that connect directly into an operator’s network (via embedded SIM and radio stack or fixed line access) are endpoints of the network. Thus, the responsibility in terms of accountability, SLAs etc., lies within the network operator (or virtual network operator).

## Slide 8
B:M2M Area Network (Device Domain):
Provide connectivity between M2M Devices and M2M Gateways, e.g. personal area network.
C: M2M Gateway:
Equipment that uses M2M capabilities to ensure M2M Devices inter-working and interconnection to the communication network.
Gateways and routers are the endpoints of the operator’s network in scenarios where sensors and M2M devices do not connect directly to the network.
Thus, the task of gateways and routers are twofold.
Firstly, they have to ensure that the devices of the capillary network may be reached from outside and vice versa. These functions are addressed by the access enablers, such as identification, addressing, accounting etc., from the operator’s platform and have to be supported at the gateway’s side as well.
Secondly, there may be the need to map bulky internet protocols to their lightweight counterpart in low-power sensor networks.

## Slide 9
D:M2M Communication Networks (Network Domain):
It covers the communications between the M2M Gateway(s) and M2M application(s), e.g. xDSL, LTE, WiMAX, and WLAN.

## Slide 10
E: Applications:
It contains the middleware layer where data goes through various application services and is used by the specific business-processing engines.
M2M applications will be based on the infrastructural assets (e.g., access enablers) that are provided by the operator.
Applications may either target at end users, such as user of a specific M2M solution, or at other application providers to offer more refined building blocks by which they can build more sophisticated M2M solutions and services. e.g. customer care functionality, elaborate billing functions, etc.
Those services, or service enablers, may be designed and offered by an application provider, but they might be offered by the operator via the operator platform itself.

## Slide 11: Requirements for M2M
Some of the general requirements for the M2M System, as specified by ETSI, are given below.
1 M2M Application communication principles: The M2M system shall be able to allow communication between M2M Applications in the Network and Applications Domain, and the M2M Device or M2M Gateway, by using multiple communication means, e.g. SMS, GPRS and IP Access. Also a Connected Object may be able to communicate in a peer-to-peer manner with any other Connected Object. The M2M System should abstract the underlying network structure including any network addressing mechanism used, e.g. in case of an IP based network the session establishment shall be possible when IP static or dynamic addressing is used.
2 Message Delivery for sleeping devices: The M2M System shall be able to manage communication towards a sleeping device.
3 Delivery modes : The M2M System shall support any cast, unicast, multicast and broadcast communication modes. Whenever possible a global broadcast should be replaced by a multicast or anycast in order to minimize the load on the communication network.
4 Message transmission scheduling: The M2M System shall be able to manage the scheduling of network access and of messaging. It shall be aware of the scheduling delay tolerance of the M2M Application.

## Slide 12
5 Message communication path selection: The M2M System shall be able to optimize communication paths, based on policies such as network cost, delays or transmission failures when other communication paths exist.
6 Communication with devices behind a M2M gateway: The M2M System should be able to communicate with Devices behind a M2M gateway.
7 Communication failure notification: M2M Applications, requesting reliable delivery of a message, shall be notified of any failures to deliver the message.
8 Scalability: The M2M System shall be scalable in terms of number of Connected Objects.
9 Abstraction of technologies heterogeneity: The M2M Gateway may be capable of interfacing to various M2M Area Network technologies.
10 M2M Service Capabilities discovery and registration: The M2M System shall support mechanisms to allow M2M Applications to discover M2M Service Capabilities offered to them. Additionally the M2M Device and M2M Gateway shall support mechanisms to allow the registration of its M2M Service Capabilities to the M2M system.
11 M2M Trusted Application: The M2M Core may handle service request responses for trusted M2M Applications by allowing streamlined authentication procedures for these applications. The M2M system may support trusted applications that are applications pre-validated by the M2M Core.

## Slide 13
12 Mobility: If the underlying network supports seamless mobility and roaming, the M2M System shall be able to use such mechanisms.
13 Communications integrity: The M2M System shall be able to support mechanisms to assure communications integrity for M2M services.
14 Device/Gateway integrity check: The M2M System shall support M2M Device and M2M Gateway integrity check. 6
15 Continuous connectivity: The M2M System shall support continuous connectivity, for M2M applications requesting the same M2M service on a regular and continuous basis. This continuous connectivity may be de-activated upon request of the Application or by an internal mechanism in the M2M Core.
16 Confirm: The M2M System shall support mechanisms to confirm messages. A message may be unconfirmed, confirmed or transaction controlled.
17 Priority: The M2M System shall support the management of priority levels of the services and communications services. Ongoing communications may be interrupted in order to serve a flow with higher priority (i.e. pre-emption).
18 Logging: Messaging and transactions requiring non-repudiation shall be capable of being logged. Important events (e.g. received information from the M2M Device or M2M Gateway is faulty, unsuccessful installation attempt from the M2M Device or M2M Gateway, service not operating, etc.) may be logged together with diagnostic information. Logs shall be retrievable upon request.

## Slide 14
19 Anonymity: The M2M System shall be able to support Anonymity. If anonymity is requested by an M2M Application from the M2M Device side and the request is accepted by the network, the network infrastructure will hide the identity and the location of the requestor, subject to regulatory requirements.
20 Time Stamp: The M2M System shall be able to support accurate and secure and trusted time stamping. M2M Devices and M2M Gateways may support accurate and secure and trusted time stamping.
21 Device/Gateway failure robustness: After a non-destructive failure, e.g. after a power supply outage, a M2M Device or Gateway should immediately return in a full operating state autonomously, after performing the appropriate initialization e.g. integrity check if supported.
22 Radio transmission activity indication and control: The radio transmitting parts (e.g. GSM/GPRS) of the M2M Device/Gateway should be able to provide (if required by particular applications e.g. eHealth) a real-time indication of radio transmission activity to the application on the M2M Device/Gateway, and may be instructed real-time by the application on the M2M Device/Gateway to suspend/resume the radio transmission activity.

## Slide 15: M2M Architecture
Three domains
• M2M Device domain,
• M2M network
• M2M Application domain

## Slide 16
M2MM Application Domain
Integration, Collaboration and M2M Application Services
Application (Reporting, Analysis, control)
Connectivity Interface (Communication and Processing Units) and Edge Computing (data element analysis and transformation)
Physical devices and Controllers (the things in IoT) [Sensors, machines, devices, Intelligent Edge nodes of Different Types
Network Domain
M2M server, device identity, device and device-network management, Data Analysis, Abstraction, Accumulation, and Management, uni-cast and multicast message delivery and core functionalities for monitoring,
Connectivity (Communication and Processing Units)
M2M Devices Domain Communication
Gateway

## Slide 17: Layer 3: M2M device communication domain
M2M Devices Domain Communication
• Gateway
• Physical devices and Controllers (the things in IoT) [Sensors, machines, devices, Intelligent Edge nodes of Different Types

## Slide 18: Layer 2: Network Domain
• M2M server, device identity, device and device-network management, Data Analysis, Abstraction, Accumulation, and Management uni-cast and multicast message delivery
• Core functionalities for monitoring
Connectivity (Communication and Processing Units)

## Slide 19: Layer 1: M2M Application Domain
•Integration, Collaboration and M2M Application Services
• Application (Reporting, Analysis, control)

## Slide 20: M2M Communication Framework
DeviceHive
Enables connecting devices to the IoTs
Web-based management software that creates security rules based networks and monitors devices

## Slide 21: M2M Protocols
• Eclipse M2M Industry Working Group Various projects
• Koneki
•Eclipse SCADA for open standards for communication protocols, tools, and frameworks

## Slide 22
ITU-T Focus Group M2M (global standardization initiative for a common M2M service layer
• Weightless (wireless communications) Group for standards and using wireless spaces for M2M

## Slide 23: M2M Usages
• Coordinated movement of tools, robots, drones
• Refinery operations, sequential control at each stage during manufacturing
• Manufacturing of food packets
• Assembly in assembly lines and
• Tracking of failures along the railway tracks.

## Slide 24: What Are the Differences Between M2M and the IoT?
By their definitions, both M2M and IoT provide remote access and communication between devices.
Neither of those interactions require human supervision.
So, while the goal is essentially the same (achieving connectivity), the means to go about achieving it are different.

## Slide 25
1. Point-to-Point vs Network-Based Access
One of the chief differences between the two connectivity technologies lies in the way communication is conducted.
M2M connectivity is achieved through point-to-point communication embedded by on-site hardware.
The Internet of Things on the other hand implies connectivity through IP networks. IoT communication of two devices, gateways, or systems can be achieved using a network protocol.
2. Reliance on Software
Another major factor in IoT vs M2M is the extent to which they rely on software.
For M2M connectivity, there is no such reliance. The technology is completely hardware-based. In order to communicate, devices don’t even need an Internet connection.
For the Internet of Things, an active connection is required. Also, while IoT relies on hardware (think environmental sensors or wearables), it requires a platform for data processing and aggregation. It’s safe to say IoT is both hardware- and software-based.

## Slide 26
3. Scalability
Scalability is another feature that showcases the difference between machine-to-machine communication and the Internet of Things.
Machine-to-machine communication has a limited number of integration options. In order to communicate, devices need to be compatible. Thus it is not possible for two machines with different tech specs to connect using M2M. That’s why technology is widely used for small-scale applications, such as maintenance.
The Internet of Things is designed with large-scale interaction in mind. As soon as a developer has a solution capable of managing communication, the number or the nature of devices is not important. There are no hardware-based integration limits for IoT implementation.

## Slide 27
4. Differences in Data Delivery
Machine-to-machine or Internet of Things communications both enable data gathering. A fundamental difference lies, however, in the way each of them process collected information.
Machine-to-machine data is usually directed towards performing a one-off task that improves the maintenance of the device. It’s not a common practice for M2M projects to transfer collected insights and integrate them into a large-scale framework.
The Internet of Things has a wider range of opportunities in terms of data visualization and analysis. All the information collected by a sensor is integrated into an analytics system where it can be compared to data gathered from other sources, broken down into insights, and otherwise analyzed. That’s why IoT is often used by businesses and governments to improve team efficiency and increase an organization’s forecasting abilities.

## Slide 28
5. Subjects of communication
Last but not least, there’s a huge difference in what kind of communication is enabled by M2M and Internet of Things communications.
Machine-to-machine communications are strictly device-based.
The Internet of Things, on the other hand, has a broader circle of possible communication subjects. Apart from devices, it can connect humans with machines, a device and a gateway, a gateway and the data system, as well as two data systems. With IoT, a device can get data from the environment around it (widely used in the automotive industry as part of the vehicle-to-everything communication model).